Deferred Snow Deformation in
Rise of the Tomb Raider
Authors of the technique:
Anton Kai Michels and Peter Sikachev

---
Idea
- Decoupling the deformation logic from geometry
- Scale well with large amount of objects
- Low memory footprint

---
Basic approach
- Render terrain and snow into heightmaps
- Render dynamic objects into deformation map
- During render, clamp the values
- Sample the deformation map during snow render

---
Deferred deformation
- Single uint32 texture
- Approximate objects by deformation points and quadratic shape
- Store deformation point height and deformation height
- deformation height = deformation point height + (distance to point)^2 × artist’s scale.

---
Deferred deformation
- Gather all deformation points
- Write deformation data around the points into the texture
- Compute shader – atomic operations → uint32 texture

---
Deferred deformation
Deformation height
Deformation point height
deformation height =deformation point height + (distance to point) 2 × artist’s scale.
Bit allocation in the texture – compatible with atomic minimum

---
Snow Rendering without elevation
- Sample deformation texture during snow render
- Snow height = min(deformation height, snow height)
  Problems:
- Mapping of the texture to the world
- Sharp deformation edges on the edge of the texture
- No elevation on the edges of the deformation

---
Elevation
- During snow render pass we have three pieces of information:
  snow height, deformation point height and deformation height
  deformation height = deformation point height + (distance to point)^2 × artist’s scale.

---
Elevation
deformation height = deformation point height + (distance to point)^2 * artist’s scale
deformation height – deformation point height = (distance to point)^2 * artists scale
distance to point = sqrt(deformation height – deformation point height)/sqrt(artists scale)
snow height – deformation point height = (depression distance)^2 * artists scale
Depression distance = sqrt(snow height – deformation point height)/sqrt(artists scale)

---
Elevation
- We computed: depression distance, depression depth and distance to point
- Elevation distance = distance to point – depression distance
- Maximum elevation distance = depression depth * artists scale
- Max elevation height = maximum elevation distance * artists scale
- Ratio = elevation distance / maximum elevation distance
- Elevation = ((0.5-2*ratio)^2+1)*height

---
Elevation

---
Video
https://youtu.be/_35eGiL0TIs?t=18